Bayesian Methodology for Structural Damage Identification and Reliability Assessment

Costas Papadimitriou, Evangelos Ntotsios

University of Thessaly, Department of Mechanical and Industrial Engineering, Volos, Greece

ABSTRACT: A Bayesian framework is presented for structural model selection and damage identification utilizing measured vibration data. The framework consists of a two-level approach. At the first level the problem of estimating the free parameters of a model class given the measured data is addressed. At the second level the problem of selecting the best model class from a set of competing model classes is addressed. The application of the framework in structural damage detection problems is then presented. The structural damage detection is accomplished by associating each model class to a damage location pattern in the structure, indicative of the location of damage. Using the Bayesian model selection framework, the probable damage locations are ranked according to the posterior probabilities of the corresponding model classes. The severity of damage is then inferred from the posterior probability of the model parameters corresponding to the most probable model class. Computational issues are addressed related to the estimation of the optimal model within a class of models and the optimal class of models among the alternative classes. Asymptotic approximations as well as Monte Carlo simulations are used for estimating the probability integrals arising in the formulation. The framework can be used for assessing the reliability of structures based on the measured vibration data. The proposed methodology is illustrated by applying it to the identification of the location and severity of damage of a laboratory small-scaled bridge using measured vibration data.

# Introduction

In structural dynamics applications there is a need for selecting and updating a theoretical model of a structure (e.g. a finite element model) that can used to make predictions of structural response and reliability (Papadimitriou et al. 2001). Moreover, a model selection and updating methodology is useful in assessing structural damage by continually updating the structural model using vibration data (Beck and Katafygiotis 1998; Sohn and Law 1997; Fritzen at al. 1998; Hemez and Farhat 1995; Lam et al. 2004; Teughels and De Roeck 2005). A Bayesian inference framework (e.g. Carlin and Louis 2000) is attractive for model selection and updating utilizing measured data. The Bayesian inference framework proposed in this work consists of a two-level approach. At the first level one proceeds with the selection of the best model class from a set of competing model classes. At the second level the free parameters of a model class are estimated given the measured data. The Bayesian framework has been successfully applied in structural identification problems using vibration measurements. In particular, asymptotic methods have been employed to address important issues related to the selection of the most appropriate model class involving the least number of parameters (Beck and Yuen 2004), as well as to study the role that the information contained in the measured data plays for constructing reliable structural models (Papadimitriou and Katafygiotis 2004).

The present work focuses on the application of the Bayesian framework in structural damage detection problems. The structural damage detection is accomplished by associating a model class to a damage location pattern in the structure, indicative of the location of damage. Applying the Bayesian model selection framework using vibration measurements, the probable damage locations are ranked according to the posterior probabilities of the corresponding model classes. The severity of damage is then inferred from the posterior probability of the model parameters corresponding to the most probable model class. Model class selection in Bayesian framework requires the estimation of multi-dimensional probability integrals. Asymptotic approximations as well as Monte Carlo simulations are presented for estimating the integrals arising in the formulation.

# Bayesian INFERENCE for model class selection

Let  be the available measured data consisting of modal frequencies  and modeshape components  at  measured DOFs, where  is the number of observed modes. Consider a family of  alternative, competing, parameterized finite element model classes, designated by , , and let  be the free parameters of the model class , where  is the number of parameters in the set . Let    be the predictions of the modal frequencies and modeshapes from a particular model in the model class  corresponding to a particular value of the parameter set .

A Bayesian probabilistic framework is next briefly presented which is attractive to address the problem of comparing two or more competing model classes and selecting the optimal model class based on the available data. The Bayesian approach to statistical modeling uses probability as a way of quantifying the plausibilities associated with the various model classes  and the parameters  of these model classes given the observed data . Before the selection of data, each model class  is assigned a probability  of being the appropriate class of models for modeling the structural behavior. Using Bayes’ theorem, the posterior probabilities  of the various model classes given the data  is

where  is selected so that the sum of all model probabilities equals to one, and   is the probability of observing the data from the model class , given by

where  is the domain of integration in  that depends on the range of variation of the parameter set , and  are the values of  at the undamaged condition of the structure. In ,  is the likelihood of observing the data from a given model in the model class . This likelihood is obtained using predictions  from the model class  and the associated probability models for the vector of prediction errors   defined as the difference between the measured modal properties involved in  for all modes  and the corresponding modal properties predicted by a model in the model class . Specifically, the model error  for the model class  is given separately for the modal frequencies and modeshapes from the prediction error equations:

where , with , is a normalization constant that accounts for the different scaling between the measured and the predicted modeshape. The model prediction errors are due to modeling error and measurement noise. Herein, they are modeled as independent Gaussian zero-mean random variables with variance . Also, given the model class , the prior probability distribution , involved in , of the model and the prediction error parameters  of the model class  are assumed to be independent and of the form .

Assuming that the prediction errors are Gaussian and independent, the likelihood in  is readily obtained in the form (Christodoulou and Papadimitriou 2007)

where

represents the measure of fit between the measured modal data and the modal data predicted by a particular model in the class , and  is the usual Euclidian norm. In deriving , the ratio between the standard deviations of the prediction errors for the modeshape components and the modal frequencies was taken for simplicity to be equal to one.

Substituting  from  for the -th model class , using the simplification that  and carrying out the integration in  over  assuming a non-informative prior distribution  for , one readily derives that

where  is a constant independent of the model class ,  is a multiplicative constant that depends on the number of data, while it is independent of the model class.

When the number of parameters is more than a few, the numerical integration in  is computationally prohibitive. In principle, one can use Monte Carlo simulations to compute the integral. In this case, an estimate of the integral is provided by the formula:

where  are uniformly distributed samples in the domain  and  are the values of  at the undamaged condition. However, Monte Carlo simulation may require a large number of samples and can be computationally inefficient. Importance sampling methods (Papadimitriou et al. 1997) can also be used to efficiently compute the integral .

Alternatively, an asymptotic approximation based on Laplace’s method (Bleistein and Handelsman 1986), can also be used to give a useful and insightful estimate of the integral in the form (Papadimitriou and Katafygiotis 2004)

where  is the value that maximizes the integrand in  or, equivalently, minimizes the function  , and  is the Hessian of  evaluated at . The probability of the model class  can be written in the form

where  is the value that minimizes the measure of fit  in ,  is constant independent of the model class , and the factor  in , known as the Ockham factor, simplifies for large number of data  to (Yuen 2002, Beck and Yuen 2004)

where it is evident that it depends from the number  of the model parameters involved in the model class . It should be pointed out that the optimisation problem for finding  for each model class are solved using efficient hybrid optimization techniques that guarantee the estimation of the global optimum (Christodoulou and Papadimitriou 2007).

It should be noted that the asymptotic approximation is valid if the optimal value  belongs to the domain  of integration in . For the cases for which this condition is violated or for the case for which more accurate estimates of the integral are required, one can use alternative stochastic simulation methods to evaluate the integral . Specifically, Monte Carlo simulation can be used which may require a large number of samples and can be computationally inefficient. Importance sampling methods (Papadimitriou et al. 1997) as well as Markov Chain Monte Carlo (Au 2001; Beck and Au 2002; Katafygiotis and Cheung 2002) may be applicable to efficiently evaluate the integral in .

The optimal model class  is selected as the model class that maximizes the probability  given by . It is evident that the selection of the optimal model class depends on the measure of fit  between the measured modal characteristics and the modal characteristics predicted by the optimal model of a model class . Thus, the first term in  gives the dependence of the probability of a model class  from how well the model class predicts the measurements. The smaller the value of , the higher the probability  of the model class . Based on the Ockham factor  simplified in , the ordering of the model classes in  also depends on the number  of the structural model parameters that are involved in each model class. Specifically, model classes with large number of parameters are penalized in the selection of the optimal model class.

Finally, the probability distribution  quantifying the uncertainty in the parameters  of a model class  given the data is obtained by applying Bayes’ theorem (Beck and Katafygiotis 1998) and then finding the marginal distribution of the structural model parameters. For the model class , this yields (Katafygiotis et al. 1998)

where  is a normalizing constant guaranteeing that the PDF integrates to one.  It is evident from  that the most probable model that maximizes the probability distribution  of the structural parameters of the model class  is the  that also minimizes the measure of fit function  in  with respect to , provided that  is selected to be constant. The most probable value of the parameter set that corresponds to the most probable model class  is denoted by .

# Damage detection methodology

The Bayesian inference methodology for model class selection based on measured modal data is next applied to detect the location and severity of damage in a structure. A substructure approach is followed where it is considered that the structure is comprised of a number of substructures. It is assumed that damage in the structure causes stiffness reduction in one of the substructures. In order to identify which substructure contains the damage and predict the level of damage, a family of  model classes  is introduced, and the damage identification is accomplished by associating each model class to damage contained within a substructure. For this, each model class  is assumed to be parameterized by a number of structural model parameters  controlling the stiffness distribution in the substructure , while all other substructures are assumed to have fixed stiffness distributions equal to those corresponding to the undamaged structure. Damage in the substructure  will cause stiffness reduction which will alter the measured modal characteristics of the structure. The model class  that “contains” the damaged substructure  will be the most likely model class to observe the modal data since the parameter values  can adjust to the modified stiffness distribution of the substructure , while the other modal classes that do not contain the substructure  will provide a poor fit to the modal data. Thus, the model class  can predict damage that occurs in the substructure  and provide the best fit to the data.

Using the Bayesian model selection framework in Section 2, the model classes are ranked according to the posterior probabilities based on the modal data. The most probable model class  that maximizes  in , through its association with a damage scenario on a specific substructure, will be indicative of the substructure that is damaged, while the most probable value  of the model parameters of the corresponding most probable model class , compared to the parameter values of the undamaged structure, will be indicative of the severity of damage in the identified damaged substructure. For this, the percentage change  between the best estimates of the model parameters  of each model class and the values  of the reference (undamaged) structure is used as a measure of the severity (magnitude) of damage computed by each model class .

The selection of the competitive model classes  depends on the type and number of alternative damage scenarios that are expected to occur or desired to be monitored in the structure. The  model classes can be introduced by a user experienced with the type of structure monitored. The prior distribution  in  of each model class or associated damage scenario is selected based on the previous experience for the type of bridge that is studied. For the case where no prior information is available, the prior probabilities are assumed to be equal, , for all introduced damage scenarios.

# Application to a small-scaled laboratory bridge section

The methodology is validated using measured modal data from a laboratory small-scaled section of a bridge shown in Figure 1a. The laboratory structure is made of steel and simulates a simply supported section of a bridge resting on rigid foundation through bearings. In order to avoid nonlinear phenomena due to sliding of the bearings during the vibration of the bridge, the faces of the bearings are glued to the foundation and the bridge deck. The bearings are simulated using square sections of White Nylon 66 material of edge size 14mm. Damage is simulated at the bearings by changing the size of the left and right bearings. This change is achieved by replacing the bearings with smaller ones of edge size 10mm.

The section of the beam at its undamaged and its damaged state was instrumented with 14 accelerometers, measuring along the longitudinal (2 sensors), vertical (8 sensors) and transverse (4 sensors) directions. The modal characteristics of the undamaged and damaged structure were obtained by analyzing measured acceleration response time histories from several impulse hammer tests using conventional modal analysis software that processes simultaneously the transfer functions at the measured locations. The damage detection methodology make use of the following five modal frequencies and modeshapes of the undamaged and damaged structure: 1st longitudinal, 1st and 2nd bending, 1st transverse and 1st torsional. The corresponding identified values of the modal frequencies are (in Hz): 108.7, 18.52, 60.08, 31.10 and 46.65 for the undamaged structure, and 69.74, 17.08, 59.22, 29.98 and 42.96 for the damaged one.

A finite element model was also constructed using beam elements to describe the behaviour of the bridge in its undamaged and damaged states. The deck and the bearings were modeled using three-dimensional two-node elements. The total number of DOF is 350. The finite element model was first calibrated to fit the modal characteristics of the undamaged structure using the model updating methodologies (Ntotsios et al. 2008). The modal characteristics of the damaged structure which contain significant information about the damaged state at the bearings were then used to predict the damage location and severity based on the proposed damage detection methodology.

(a)	                  (b)

Figure 1: (a) Small scale section of bridge with sensors, (b) Finite element model.

Based on the damaged detection methodology, nine (9) competitive model classes , given in Table 1, were introduced to monitor various probable damage scenarios corresponding to single and multiple damages at different substructures. The stiffness related parameters used in each model class involve the modulus of elasticity  of the deck, the modulus of elasticity  of the bearings and the cross-sectional moment of inertia  and  of the bearings with respect to the global coordinate system shown in Figure 1b. All model classes are generated from the updated finite element model of the undamaged structure. Based on the parameterization shown in Table 1, it is expected that the methodology will give as the most probable model class one of , ,  and  that contain the actual damage. The results for the probability of each model class and the value of the measure of fit , given in , between the measured and the optimal model predicted modal characteristics for all model classes, are also reported in Table 1.

Table 1: Probability  of each model class and predicted magnitude of damage  (%).

| Model Class |  | Prob. | Fit | Parameters | Damage (%) |
| --- | --- | --- | --- | --- | --- |
|  | 1 | 0 | 0.1444 | deck | -14.1 |
|  | 1 | 0.029 | 0.0223 | left bearing | -68.4 |
|  | 1 | 0.003 | 0.0241 | right bearing | -67.7 |
|  | 1 | 0.708 | 0.0202 | left & right bearings | -55.2 |
|  | 2 | 0.239 | 0.0184 | deck | +6.93 |
|  |  |  |  | left & right bearings | -54.3 |
|  | 2 | 0.000 | 0.0299 | bearings | -52.1 |
|  |  |  |  | bearings | -53.3 |
|  | 2 | 0.014 | 0.0201 | left bearings | -58.4 |
|  |  |  |  | right bearings | -51.8 |
|  | 3 | 0 | 0.0280 | deck | -3.31 |
|  |  |  |  | bearings | -52.6 |
|  |  |  |  | bearings | -54.2 |
|  | 3 | 0.007 | 0.0180 | deck | +7.13 |
|  |  |  |  | left bearings | -58.9 |
|  |  |  |  | right bearings | -49.3 |

Comparing the probability  of each model class and also the corresponding magnitude of damages  predicted by each model class it is evident that the proposed methodology correctly predicts the location and magnitude of damage. Among all alternative model classes , ,  and  that contain the actual damage, although the model classes  and  predict the smallest measure of fit , the proposed methodology favors with probability 0.708 the model class  with the least number of parameters, which is consistent with theoretical results available for Bayesian model class selection (Beck and Yuen 2004). The reduction of 55.2% of the modulus of elasticity at the left and right bearings, predicted by the most probable model class , is an indication of the severity of damage caused by reducing the edge length of the bearings from 14mm to 10 mm. The model class  is the second most probable model class, involving two parameters, favored with probability  and correctly predicts the magnitude of damage to be 54.3%, at approximately the same level as that predicted by the most probable model class . The third most probable model class , although it does not contained the damage, it is favored by the methodology in relation to the other two model classes  and  that contain the damage. The model class  predicts damage of magnitude 68.4% at the left bearing, while by construction it fails to predict damage at the right bearing since there are no parameters in this model class to monitor changes in the right bearings. The model classes  and , involving two and three parameters, respectively, also correctly predict the magnitude of damage to be at the same levels (approximately 59% at the left bearing and 49% to 52% at the right bearing) as that predicted by the most probable model class . The slight differences in the predictions from the model classes that contain the damage and the slight increase of the stiffness for the deck, of the order of 7%, predicted from model classes  and  are due to the measurement and model errors.

# conclusions

A Bayesian inference framework for structural model selection and updating using vibration measurements was presented and applied to the identification of the location and severity of damage of structures using measured modal data. The effectiveness of the damage detection methodology was illustrated using measured vibration data from a small-scaled laboratory section of a bridge. Results provided useful information on the strength and limitations of the methodology. The effectiveness of the methodology depends on several factors, including the model classes and parameterization that are introduced to simulate the possible damage scenarios,  the type, location and magnitude of damage or damages in relation to the sensor network configuration, as well as the model and measurement errors in relation to the magnitude of damage. Damages of relatively small magnitude may be hidden and difficult to be identified. Damage predictions can be improved by introducing high fidelity finite element model classes and estimation algorithms that provide more accurate values of the modal characteristics.

# Acknowledgements

This research was co-funded 75% from the European Union (European Social Fund), 25% from the Greek Ministry of Development (General Secretariat of Research and Technology) and from the private sector, in the context of measure 8.3 of the Operational Program Competitiveness (3rd Community Support Framework Program) under grant 03-ΕΔ-524 (PENED 2003). This support is gratefully acknowledged.

# References

Au, S.K. 2001. On the solution of the first excursion problem by simulation with applications to probabilistic seismic performance assessment. Ph.D. Thesis, EERL Report 2001-02, Caltech, Pasadena, CA.

Beck, J.L.  and Au, S.K. 2002. Bayesian updating of structural models and reliability using Markov chain Monte Carlo simulation. Journal of Engineering Mechanics, ASCE, 128 (4), p. 380-391.

Beck, J.L. and Katafygiotis, L.S. 1998. Updating models and their uncertainties. I: Bayesian statistical framework. Journal of Engineering Mechanics, ASCE, 124 (4), p. 455-461.

Beck, J.L. and Yuen, K.V. 2004. Model selection using response measurements: Bayesian probabilistic approach. Journal of Engineering Mechanics, ASCE, 130(2), p. 192-203.

Bleistein, N. and Handelsman,  R.1986. Asymptotic expansions for integrals. Dover, New York.

Carlin, B.P. and Louis, T.A. 2000. Bayes and empirical Bayes methods for data analysis. Second Edition, Chapman & Hall/CRC, New York.

Christodoulou, K. and Papadimitriou, C. 2007. Structural identification based on optimally weighted modal residuals. Mechanical Systems and Signal Processing, 21, p. 4-23.

Fritzen, C.P., Jennewein, D. and Kiefer, T. 1998. Damage detection based on model updating methods. Mechanical Systems and Signal Processing, 12(1), p. 163-186.

Hemez, F.M. and Farhat, C. 1995. Structural damage detection via a finite element model updating methodology. The International Journal of Analytical and Experimental Modal Analysis, 10(3), p. 152-166.

Katafygiotis, L.S. and Cheung, S.H. 2002. MCMC based simulation methodology for reliability calculations. Fourth International Conference on Computational Stochastic Mechanics, Spanos P.D., and Deodatis G., (Eds). Millpress, Rotterdam, the Netherlands, p. 293-299.

Katafygiotis, L.S., Papadimitriou, C. and Lam, H.F. 1998. A probabilistic approach to structural model updating. International Journal of Soil Dynamics and Earthquake Engineering, 17(7-8), p. 495-507.

Lam, H.F., Katafygiotis, L.S. and Mickleborough, N.C. 2004.  Application of a statistical model updating approach on phase I of the IASC-ASCE structural health monitoring benchmark study. Journal of Engineering Mechanics (ASCE), 130(1), p. 34-48.

Ntotsios, E., Karakostas, Ch., Lekidis, V., Panetsos, P., Nikolaou, I., Papadimitriou, C. and Salonikos, Th. 2008. Structural identification of Egnatia Odos bridges using ambient and earthquake-induced vibrations. Bulletin of Earthquake Engineering, doi:10.1007/s10518-008-9074-5

Papadimitriou, C. and Katafygiotis, L.S. 2004. Bayesian modeling and updating. In Engineering Design Reliability Handbook, Nikolaidis N., Ghiocel D.M., Singhal S. (Eds), CRC Press.

Papadimitriou, C., Beck, J.L. and Katafygiotis, L.S. 2001. Updating robust reliability using structural test data. Probabilistic Engineering Mechanics, 16(2), p. 103-113.

Papadimitriou, C., Beck, J.L. and Katafygiotis, L.S. 1997. Asymptotic expansions for reliability and moments of uncertain systems. Journal of Engineering Mechanics, ASCE, 123(12), p. 1219-1229.

Sohn, H. and Law, K.H. 1997. Bayesian probabilistic approach for structural damage detection. Earthquake Engineering and Structural Dynamics, 26, p. 1259-1281.

Teughels, A. and De Roeck, G. 2005. Damage detection and parameter identification by finite element model updating. Archives of Computational Methods in Engineering, 12(2), p. 123-164.

Yuen, K.V. 2002. Model selection identification and robust control for dynamical systems. Ph.D. Thesis, EERL Report 2002-03, Caltech, Pasadena.

# Text boxes

y

x

z